## Slide 1
Analysis of aerosol behavior inside containment during severe accidents
Particles deposition model include
following mechanisms
Gravitational settling (sedimentation)
Brownian diffusion
Diffusiophoresis
Thermophoresis
Multicomponent aerosols condensation block
Multicomponent aerosols coagulation block
Aerosol deposition block
M. Zatevakhin, I. Ivkov
Saint Petersburg Research and Design Institute ATOMENERGOPROEKT
Aerosol code consist of

## Slide 2: Coagulation processes: numerical method
Semi-implicit version of Modified Kovetz-Olund method (Stankova E.N., Zatevakhin M.A. The modified Kovetz and Olund method for the numerical solution of stochastic coalescence equation. Proceedings 12th International Conference on Clouds and Precipitation, Zurich, 19-23 August 1996, P. 921-923) .
 Solution is positive at any t

## Slide 3: Coagulation processes: validation tests
Species mass distributions functions. Mi0 are initial distributions, Mi are final distributions, Mtotal is the total mass, Analitical is analytical solution (Golovin, A.M. The solution of the coagulation equation for cloud droplets in a rising air current. Bull. Acad. Sci. USSR, Geophys. Ser. 1963. No 5. P. 482-487 ).

## Slide 4: Coagulation processes: validation tests
Comparison with results of (Yang Zhang, C. Seigneur, J. H. Seinfeld, J. H. Jacobson and F. S. Binkowski. Simulation of aerosol dynamics: a comparative review of algorithms used in air quality models. Aerosol Science and Technology. 1999. Vol. 31. P. 487-514).

## Slide 5: Coagulation: influence of dilution: coagulation “freezing”
Monodisperse distribution,
D0 = 1 m, Tcoagul= 6 sec

## Slide 6: Coagulation: fluctuation of concentration: the process is practically linear!
Parameter | 
Median diameter (m ) | 
Dn | 0.038
Da | 0.32
Dc | 5.7
Standard derivation | 
n | 1.8
a | 2.16
c | 2.21
Total volume (m3 cm-3) | 
Vn | 0.63
Va | 38.4
Vc | 30.8
Polluted urban conditions:
sum of three log-normal
distributions, Tcoagul= 350 sec

## Slide 7: Coagulation in the presence of external sources

## Slide 8
Comparison with MELCOR simulations

## Slide 9: Condensation processes: numerical method
Jacobson, M.Z. (1997). Numerical Techniques to Solve Condensational and Dissolutional Growth Equations When Growth is Coupled to Reversible Reactions, Aerosol Sci. Technol. 27: 91-498.
; i=1,…,Np-1
; i=1,…,Np-1, j=1,…,Nc

## Slide 10: Condensation processes: validation tests
Comparison with results of (Yang Zhang, C. Seigneur, J. H. Seinfeld, J. H. Jacobson and F. S. Binkowski. Simulation of aerosol dynamics: a comparative review of algorithms used in air quality models. Aerosol Science and Technology. 1999. Vol. 31. P. 487-514).

## Slide 11: Condensation processes: multi-component particles

## Slide 12: Results of calculations aerosol parameters using of aerosol code integrated with KUPOL-M thermohydraulic code
Aerosol distribution within control volume at Dnom346-break + SBO
Comparison between calculated aerosol output (1) and data obtained according to project recommendations (2).

## Slide 13: Simulation of coagulation process in convective boundary layerатмосферы. (comparison of 3D LES и 1D diffusion models)
Computational domain: X=4000 m, Y=4000 m, Z=2400 m.
Grid: Nx×Ny×Nz = 74×74×45 cells.
Periodic conditions is used on vertical boundaries.
At the lower surface universal functions are applied with a roughness z0 = 0.16 m and kinematic heat flux Qs=0.06 K m/s. A stress-free upper boundary was used.
The initial mean temperature profile represents a constant-temperature mixed layer topped by a layer of uniform stability: θ = 26.6 °C for z = 0…1350.4 m and then θ constantly increases with gradient 0.003 K/m.
Fixed flux of 3.5e-4 kg/(m2s) of 0.05 m monodiperse particles with density of 2160 kg/m3 was applied after 2500 sec convection development
Mass grid consists of 20 bins range from 0.05 to 2.5 m.
3D LES problem formulation

## Slide 14: Simulation of coagulation process in convective boundary layerа.
3D LES total mass concentration evolution (animation)

## Slide 15: Simulation of coagulation process in convective boundary layer. (comparison of 3D LES и 1D diffusion models)
1D diffusion model
where:
Z – vertical coordinate,
Mj – j-th bin particles density,
Qj –source term describing coagulation process,
KD(Z) – turbulent diffusion coefficient, defined by LES results as follows:
<…> - horizontal averaging operator at level Z,
KDSGS - subgrid diffusion coefficient.

## Slide 16: Simulation of coagulation process in convective boundary layerа. (comparison of 3D LES и 1D diffusion models)
Fig. 1. Total mass concentration
Fig. 2. Total number concentration
Fig. 3. Mean particle radius
Fig. 4. Particles distribution function

## Slide 17: Simulation of coagulation process in convective boundary layerа.
Instantaneous distribution of particles mean radius

## Slide 18: Possible farther development
  Take into account aerosol hygroscopicity
  Integrate aerosol code with 3D hydrodynamic code
  Use new experimental data for code validation