## Slide 1: ISTC project #3345: Ex-Vessel Source Term ANalysis (EVAN) Status and Workplan Presentation Vladimir Bezlepkin, Yuri Leontiev (SPAEP) Arkady Kiselev (IBRAE) Sevostian Bechta (NITI) Oleg Krektunov, Mikhail Lebedev, Lev Feldberg (CKTI) Natalia Ampelogova (VNIPIET)
9th Meeting of EU-ISTC Contact Expert Group on Severe Accident Management (CEG-SAM)
7-9 March 2006
Paris, France

## Slide 2: Presentation Outline
Introduction
Overall Project Description
  Project Tasks Breakdown
  Outcome of EVAN kick-off meeting
Next steps
Conclusions

## Slide 3: Project tasks list
WP1/Task 1: Analysis of Severe Accident Scenarios (SPAEP, IBRAE)
WP2: Molten pool/core catcher FP release
  Task 2: Experimental investigations (NITI)
  Task 3: Theoretical and numerical modeling (IBRAE)
WP 3: Primary aerosol transport/deposition
  Task 4: Experimental investigations (NPO CKTI)
  Task 5: Theoretical and numerical modeling (SPAEP, IBRAE)
WP 4: Containment parameters impact on iodine species behaviour
  Task 6: Experimental investigations (VNIPIET)
  Task 7: Theoretical and numerical modeling (VNIPIET, SPAEP)

## Slide 4: Task 1: Analysis of Earlier Results of Severe Accident Scenarios Calculations.
Participants: SPAEP, IBRAE
Analysis of plant calculations results for VVER and PWR applications
  Data provided by foreign collaborators (Western LWRs, VVER-1000, Phebus (ISP-46), SARNET (PSA-2 and OPTSAM data)
  Data alrady available to Russain participants (VVER-640, VVER-1000)
Providing bounding parameters ranges for experiments (Tasks 2, 4, 6)
Justification of applicability of the proposed results for validation of models
List of data provided by collaborators (who provides what)

## Slide 5: Task 2: Experiments on Fission Product Release from Molten Pool
Research team: NITI (Prof. V.Khabensky, Dr.S.Bechta, Dr.V.Gusarov, S.Vitol and others)
Low-volatile FP release from molten pool during its transition from sub-oxidized (C-30) to fully-oxidized (C-100) state
Main medium-scale tests -- NITI
Support analytical tests -- ISC RAS
Basically agreement is reached for Phase 1 test specifications
GEMINI-2006 pre-calculations needed

## Slide 6: Methodology
Main tests:
- medium-scale tests with chemically prototypic molten corium (~2 kg),
- power deposited in the melt is simulated by the melt induction heating in a cold crucible (IMCC),
- flow method for release rate determination
Illustration of an analytical system used in the LPP project
1. Shielded box. 2. Metallic bottom. 3. Molten corium. 4. Inductor. 5. Cold crucible. 6. Quartz tube. 7. Cooled cover. 8. Start-up medium area filter (MAF). 9. Side port of the cover. 10. Vacuum pump. 11, 19, 20, 37. Regulating valves. 13. Analytical line rotameter. 12,25. Roll-blade flow meter. 14. Pressurized gas tanks (air, nitrogen). 15,16,24,34. Pressure sensors. 17,26,27,31,35. L thermocouples. 21. Analytical filters F1 (AFA). 22. Medium-area filters F2 (MAF). 23. Three-way cock. 28. Vibrator. 29. Analytical line. 30. Main line. 32. Cyclone. 33. Large-area filter F3 (LAF). 38. Disposable specimen holder. 39. Disposable module.

## Slide 7: Task 3: Analytical support of FP release experiments
Participants: IBRAE (Dr.A.Kiselev’s team)
Pre-test calcs for experiments and follow-up analysis
Justification of applicability of the proposed results for validation of models

## Slide 8: Task 4: Experimental investigation of selected aerosol transport problems for severe accident conditions
Research team: NPO CKTI (Dr.Krektunov group, multiphase flows and diagnostics)
Deposition/resuspension of aerosols in primary circuit pipes in varying flow conditions
Main tests — CKTI
Supportive analytical tests on properties of generated aerosol particles — SPb Tech Uni
Varying Re 1200-10000, particles size
Applicable to validation of DNS/LES models
Simpler aerosols (NH4Cl), known stickiness
Developing universal expt technique

## Slide 9: Closed-loop circuit with optical instrumentation for two-phase flow diagnostics
Capability to build curcuits of complex geometry (primary circuit LEGO™):
  Pipes of various diameter and orientation, bends, inlet/outlet conditions (chambers), aerosol sources locations
  Easy assembly/disassembly
Extended (reasonably) boundary conditions
  Thermal conditions, carrier media, materials and characteristics of surfaces
Limited number of aerosol types

## Slide 10: Task 5: Analytical Support of Experiments
SPAEP computational mechanics group in NPP safety research department
  Mechanistic aerosol kinetics models coupled to 2D and 3D CFD models (DNS or LES-based)
IBRAE severe accident research lab
  integral aerosol models coupled to RATEG/SVECHA/GEFEST code
Deliverables: reports on pre-test calcs for experiments and follow-up analysis, justification of applicability of the expt results for validation of models

## Slide 11: Task 6: Experiments on Containment Parameters Impact on Volatile Iodine Species Behaviour
Participants: VNIPIET (experimental teams for iodine chemistry research)
Experiments on containment sump solution with sludge presence
Varying pH, T, irradiation
Sludge content agreed upon
Well-controlled conditions, single effect tests for direct comparison
Two basic experimental techniques (single-autoclave and multi-ampoule) to be worked out for Phase 2

## Slide 12: Task 7: Analytical Support of Experiments
Participants: VNIPIET, SPAEP
  Severe accident containment iodine behaviour model developed by VNIPIET/SPAEP
  Codes for solution рН and Еh (redox) calculation, published data, iodine databases.
Pre-test calcs for experiments and follow-up analysis
Justification of applicability of the proposed results for validation of models

## Slide 13: EVAN Project Status & Schedule
Phase 1 (1 year) Mounting/installation, pilot expertiments and analysis
  Financial: ISTC support obtained
  Technical: Work plan for Stage 1 is drafed. Expts specifications and collaborators’ input to be finalised here.
  Contractual: in March Workplan to be sent to ISTC for Project Agreement preparation (+1-2 month for signing PA)
Phase 2 (2 years) More detailed testing & analysis selected on the evaluation of Phase 1 results
  Proposal preparation — 3rd-4th quarter of Phase 1

## Slide 14: March 31 – final drafting of EVAN workplan to be sent to ISTC By that time we definitely need:
Final list of collaborators with support letters sent to ISTC and a copy to SPAEP
List of data provided by collaborators for Task 1 (who provides what)
Recommendations for tests matrices (Tasks 2, 4, 6) clarifying and deepening the response from collaborators at the EVAN kick-off meeting

## Slide 15: Thanks
To collaborators
To Russian colleagues
To CEG-SAM chairs
To EdF host