## Slide 1: ISTC/SPAEP Research Projects
ISTC CEG-CM Meeting,
February 2004
CEA, Paris, France

## Slide 2: Presented by
Yuri Leontiev
Head of Radiological Safety Lab
Research and Development Department
Institute ATOMENERGOPROEKT (SPAEP)
phone: +7 (812) 567-95-03
fax : +7 (812) 567-90-32
e-mail: yuri.leontiev@nio.spbaep.ru

## Slide 3: Presentation Outline
Introduction
Overall Project Description
  Main results expected
  Project tasks list
  Institutes involved
  Needs for CEG consulting/advice
Project Tasks Breakdown
Conclusions

## Slide 4: Overall Project Description
Name: Ex-Vessel Source Term ANalysis (EVAN)
ISTC Field Codes: ENV-MRA, FIR-EXP, FIR-MOD
Goal: Severe accident in-containment and environmental source term assessment along with radiological consequences for plants/sites of interest.
Features: Extra investigation of some ex-vessel stage phenomena with high impact on the source term/consequences identified by earlier international research (for example, in FP4 STU project).
Notes: Comprises: Assessment of consequences of late phase fission product release to the PWR containment atmosphere at the ex-vessel stage of the severe accident for real systems

## Slide 5: Project tasks list
Task 1: Reference severe accident scenario choice and analysis
Task 2: Molten pool FP release analysis
Task 3: Local aerosol behaviour analysis
Task 4: Iodine species behaviour analysis
Task 5: Environmental source term assessment and consequences analysis

## Slide 6: Partner organisations (name and location)
SPAEP (Research and Design Institute ATOMENERGOPROEKT, St.Petersburg)
NITI (Alexandrov Research Institute of Technology, Sosnovy Bor)
IHPCDB (Institute for High Performance Computing and Data Bases, Polytechnical University, St.Petersburg)
VNIPIET (All-Russian Design and Research Institute of Complex Power Technology, St.Petersburg)
KRI (Khlopin Radium Institute, St.Petersburg)

## Slide 7: Partner organisations (Applicable field of expertise)
SPAEP (Design of NPPs with VVER and FBR, safety assessment, severe accidents research, R&D programs coordination)
NITI (PWR severe accidents research, experimental facilities)
IHPCDB (CFD codes development, supercomputer applications, applied software engineering)
VNIPIET (Design of NPPs with GMR, radiochemistry, radwaste treatment, experimental facilities)
KRI (Dose and risk analysis, environmental impact assessment)

## Slide 8: Expected CEG contribution
Choice of plant/site of interest
Choice/discussion of reference scenario
Discussion on project goals
Adjusting scope of work
Linking with other ISTC and EC projects
Proposals on collaborators
Other…

## Slide 9: Choice and Analysis of the Reference Accident Sequence: Task 1 (1)
Participants: SPAEP, NITI
Stages:
  Analysis of fission products build-up and decay in the irradiated fuel
  Justification of choosing the reference accident sequence. Analysis of in-vessel severe accident stage (reactor plant analysis)
  Analysis of corium behaviour in the reactor cavity (if necessary, including interaction with sacrificial material)
  Containment parameters analysis

## Slide 10: Choice and Analysis of the Reference Accident Sequence: Task 1 (2)
Tools used for task implementation:
  SAPPHIRE and RC codes, libraries of reaction rate constants and core neutron fields
  RATEG/SVECHA/GEFEST, MELCOR codes. Expert analysis
  CORCAT, DINCOR codes
  CUPOL-M lumped parameter code
Deliverables: Report on input data for ex-vessel phase source term assessment

## Slide 11: Task 1 in Brief
Choice and analysis of the reference accident sequence
Input data for late phase in-containment and environmental source term assessment:
  for both new and existing NPP designs
  in-vessel phase analysis – unified (“frozen”) approach

## Slide 12: Numerical Modelling of Local Aerosol Deposition Processes: Task 2 (1)
Participants: SPAEP, IHPCDB
Stages:
  Analysis of aerosol transport and kinetics for the area above the molten pool
  Analysis for local aerosol deposition problems (different removal processes)
  Analysis of the parameters used for constitutive relations in the aerosol models for lumped-parameter codes
Notes:   Assessment of the characteristic ranges and recommendations for choice of the parameters used for constitutive relations in the aerosol models for lumped-parameter codes used for severe accident environmental source term analysis.

## Slide 13: Numerical Modelling of Local Aerosol Deposition Processes: Task 2 (2)
Tools used for task implementation:
  2D and 3D CFD models coupled with aerosol kinetics models
Deliverables: Report on generic numerical models for local aerosol transport and deposition for severe accident conditions

## Slide 14: Task 2 in Brief
Local Aerosol Kinetics, T/H coupled
Generic aerosol transport and deposition modelling results for severe accident conditions
  Recommendations for aerosol models in lumped parameter containment codes
  Refined aerosol transport results for local containment areas of interest (melt location etc.)
  Necessary for representative experimental results

## Slide 15: Experiments on Fission Product Release from Molten Pool: Task 3 (1)
Participants: SPAEP, NITI
Stages:
  Experiments on low volatile fission product (Ru, Sr, Ba, La, Ce and Mo) release from molten pool with water supply onto the melt surface. Corium composition is chosen according to the reference accident scenario based on Task 1 results.
  Experiments on reducing the low volatile fission product release from molten pool by special additives to the sacrificial material (when appropriate)

## Slide 16: Experiments on Fission Product Release from Molten Pool: Task 3 (2)
Tools used for task implementation:
  RASPLAV experimental facilities for investigation of high-temperature processes in corium equipped with aerosol sampling system
  Various equipment for preparing experiments, carrying-out the post-test analysis and processing of experimental results
Deliverables: Reports on experiments

## Slide 17: Task 3 in Brief
Molten pool fission product release expts
Experimental data on MPFPR for/with:
  Both new and existing NPP designs
  Water supply onto the melt
  FP aerosols transport from melt location over containment volumes
  Optimisation of sacrificial materials compositions (if any)

## Slide 18: Assessment of Containment Parameters Impact on Volatile Iodine Species Behaviour: Task 4 (1)
Participants: SPAEP, VNIPIET, NITI
Stages:
  Analysis of separate models, numerical techniques, and rate constants impact on overall uncertainty of severe accident iodine source term
  Experiments on containment sump solution/sludge effect on gas phase volatile iodine species content and proportioning.
  Experiments for determination of the water/gas phase partitioning coefficients of water solution components
Notes:   Uncertainty analysis of content and proportioning of the gas phase iodine species for severe accident conditions. Recommendations on choice of numerical models and rate constants values for severe accident environmental source term assessment

## Slide 19: Assessment of Containment Parameters Impact on Volatile Iodine Species Behaviour: Task 4 (2)
Tools used for task implementation:
  VNIPIET and NITI experimental setups for iodine chemistry research
  Severe accident containment iodine behaviour model developed by VNIPIET/SPAEP
  Codes for solution рН and Еred-ox calculation, published experimental and calculation data, databases on iodine rate and equilibrium constants, proprietary unpublished data. SILOXID sorbent to determine proportions of molecular iodine and organic iodine in the gas phase.
Deliverables: Analytical report and reports on research results for stages 2, 3

## Slide 20: Task 4 in Brief
Volatile iodine species behaviour
Experimental and analytical data
  Impact of sump solution on volatile iodine species present in the containment atmosphere
  Recommendations on radioiodine release suppression
  Applicable for new/existing designs (NPPs with VVER, conditions of MCCI, presence of Fe- and Si- species in sump solution)

## Slide 21: Accident Environmental Release and Doses Assessment: Task 5 (1)
Participants: SPAEP, KRI
Stages:
  Analysis of containment processes and environmental source term assessment for the reference scenario
  Analysis of compliance for scope and amount of environmental source term results for application in risk assessment studies ( based on MACCS and PC-COSYMA techniques, Russian materials, and international documents on PSA-2 and PSA-3 requirements)
  Dose assessment for population due to severe accident (reference NPP site)

## Slide 22: Accident Environmental Release and Doses Assessment: Task 5 (2)
Tools used for task implementation:
  ASTRA-C and MELCOR codes
  MACCS and PC-COSYMA codes
  Expert analysis
Deliverables: Report on radiological consequences of the reference severe accident scenario for reference NPP site

## Slide 23: Task 5 in Brief
Assessment of environmental source term (EST) and its consequences
Analysis of SA radiological impact
  Consistent estimation of late phase EST
  Can be site-specific or generic/probabilistic
  Analysis of severe accident consequences mitigation measures

## Slide 24: Conclusions and thanks
To CEA host and CEG-CM experts, and to A.Zurita, L.Tocheny and our NITI colleagues personally

## Slide 25: And again, expected CEG/SAM contribution
Choice of plant/site/system of interest
Choice/discussion of reference scenario
Discussion on project goals
Adjusting scope of work
Linking with other ISTC and EC projects
Proposals on collaborators
Other…