## Slide 1
Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident
Leonid I. Zaichik
Nuclear Safety Institute of the Russian Academy of Sciences Moscow, Russia
1

## Slide 2: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
The deposition rate on walls is determined with due regard for all
essential mechanisms that can take place in the reactor circuit:
Brownian and turbulent diffusion;
Turbulent migration (turbophoresis) induced by turbulence energy gradient;
Gravitational sedimentation;
Thermophoresis caused by temperature gradient;
Convective transfer due to vapour condensation onto walls (diffusiophoresis);
Lift force due to velocity gradient of the carrying flow;
And centrifugal force when flowing around a curved surface or
in the case of flow swirl;
Our objective is to present models for predicting the deposition of aerosol-shaped fission products.
2

## Slide 3: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
Motion Equation of an Aerosol Particle
fluid velocity Brownian force
particle response time
body force
3

## Slide 4: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
Kinetic Equation for the Particle Velocity PDF
turbulenceparticle interaction Brownian motion
P(xi ,vi ,t) is the probability of finding a particle at a point xi , with a velocity vi , at time t
uiuj  is the fluid turbulent stress
 Ui/ xj is the averaged velocity gradient of the fluid
fu ij , lu ij , mu ij , gu ij , and hu ij are the tensor coefficients that quantify a response of a particle to the fluid turbulence (coupling between the fluid and particulate phases)
4

## Slide 5: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
Equation for the mean particle velocity Vi
Conservation Equations of Mass and Momentum
Equation for the particle concentration 
particulate stresses
5

## Slide 6: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
Algebraic relation for the third-order moments of particle fluctuating velocities
Conservation Equation of the Particulat Stresses
Transport equation for the second-order moments of particle fluctuating velocities (particulate stresses)
Variation in time Convection Diffusion Production from the mean motion
Turbulenceparticle interactions Brownian motion
This second-moment model provides the basis for predicting deposition rates of aerosol particles.
6

## Slide 7: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
The deposition coefficient
The deposition rate
Definition of the Aerosol Deposition Rate
Ω is the volume considered, S is the surface bounding the volume considered, Jw is the total deposition flow rate on the wall, κ is the sticking coefficient that is equal to the ratio between the flow rate of aerosols sticking the wall and the total deposition flow rate on the wall
b is the bulk aerosol concentration, u* is the friction velocity
7

## Slide 8: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
The deposition coefficient
The Deposition Rate due to Brownian and Turbulent Diffusion
ScBf /DB is the Schmidt number defining as the ratio of the fluid kinematic viscosity to the Brownian diffusivity
In the case of Brownian and turbulent diffusion, the deposition coefficient corresponds to the mass transfer coefficient, which takes place at high Schmidt numbers for the forth-order extent law of the fluid turbulent diffusivity in the viscous sub-layer (Levitch, 1962).
8

## Slide 9: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
The deposition coefficient
The Deposition Rate due to Turbulent Migration (Turbophoresis)
ρp and ρf are the particle and fluid densities, dp is the particle diameter, Kn is the Knudsen number defined as the double molecule free path to the particle diameter;
A1=1.20, A2=0.41, A3=0.88 (Talbot et al., 1980)
The particle response time
9

## Slide 10: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
The Deposition Rate due to Turbulent Migration (Turbophoresis)
The deposition coefficient against the dimensionless particle response time in channel flows
1  model prediction, 2  empirical correlation by McCoy & Hanratty (1977), 3  DNS by Uijttewaal & Oliemans (1996), 4  experiment by Liu & Agarwal (1974), 5  DNS by McLaughlin (1989), 6  DNS by Wang et al. (1997)
10

## Slide 11: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
The Deposition Rate due to Diffusion and Turbulent Migration (Turbophoresis)
The deposition coefficient against the dimensionless particle response time in channel flows
1  Re=1.5·105, B=5·105; 2  Re=6·104, B=1.2·106; 3  Re=1.5·104, B=4.2·106; 4  experimental data by McCoy & Hanratty (1977)
11

## Slide 12: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
bV+ / j+0 measures the ratio of the deposition coefficients due to the convectionforce and diffusionmigration mechanisms, Vw is the deposition rate caused by the convectionforce mechanism (V+ =Vw /u* ), j+0 is the deposition coefficient when Vw=0
λp and λf are the particle and fluid conductivity coefficients;
C1=1.17, C2=1.14, C3=2.18 (Talbot et al., 1980)
The deposition rate cased by the thermophoresis force
The Deposition Rate due to DiffusionMigration and ConvectionForce Mechanisms
12

## Slide 13: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
The force balance
The Sticking Coefficient
Fs is the detachment force due to fluid wall stresses, Fa is the retention force due to adhesion, σw is the wall stress, dp is the particle diameter, Σ is the adhesion energy
The sticking coefficient
The probability of wall stress fluctuations
13

## Slide 14: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
The Effect of Thermophoresis on Aerosol Deposition
The deposition efficiency against the diameter of aerosols
13 – predictions with no resuspension (κ=1); 46 – predictions with resuspension; 79 – experiments by Byers (1967); 1, 4, 7 – T0 =505 К; 2, 5, 8 – T0=630 К; 3, 6, 9 – T0 =755 К
14

## Slide 15: Modelling of Aerosol Deposition in a Nuclear Reactor during a Severe Accident (Task5)
Summary
On the basis of comparisons with experimental data and numerical simulations, it can be concluded that the models presented correctly reproduce the main tendencies of the effect of diffusionmigration and convectionforce mechanisms on the aerosol deposition rate in channel turbulent flows.
The models for predicting the deposition rate of aerosol particles are implanted in the PROFIT code, which was elaborated at the Nuclear Safety Institute of the RAS.
15