## Slide 1: S. Guentay
19. CEG-SAM Meeting
March 14-17, 2010
Pisa, Italy
Containment thermal-hydraulics of current and future LWRs for severe accident management
ERCOSAM

## Slide 2: Outline
  Containment hydrogen issue
  ERCOSAM: addressing better understanding margins for hydrogen management possibilities
  Project partners
  Current Status

## Slide 3: Containment hydrogen issue
The presence of a stratification in a NPP containment is a source of concern, as pockets of hydrogen in high concentration could lead to a deflagration or detonation risk which might challenge several equipment necessary for safety functions and even the containment structural integrity.
The objectives of ERCOSAM:
establish whether in a test sequence representative of a severe accident in a LWR, well chosen from existing plant calculations, a hydrogen (helium) stratification can be established during part of the transient starting from the initiation of the loss of coolant accident (LOCA) blowdown until the end of bulk hydrogen release from the reactor vessel into the containment,
how this stratification can be broken down by the operation of Severe Accident Management systems (SAMs); sprays, coolers and Passive Auto-catalytic Recombiners (PARs).

## Slide 4: ERCOSAM: addressing better understanding margins for hydrogen management possibilities (1)
Two tier approach
Experiments in four containment simulators with very small to very large scales at conditions scaled down prototypical accident conditions in real plants
Planning, pre- and post test calculations using 3D, CFD and lumped parameter codes to gain improved confidence in the codes for future plant safety analyses (PSA L2, plant behavior, assessment and design of SAM measures for hydrogen management)

## Slide 5: ERCOSAM: addressing better understanding margins for hydrogen management possibilities (2)
Experiments planned at
“small scale” TOSQAN (IRSN, Saclay),
"medium scale" in the MISTRA (CEA, Saclay),
“large scale”in PANDA (PSI, Villigen) and
"nearly prototypical scale" in the KMS-like facility (only for code benchmarking)

## Slide 6: Project partners
ERCOSAM
PSI
IRSN
CEA
NRG
KIT
AECL
SAMARA
IBRAE
IPPE
Consortium Agreement
Coordination Agreement
Uni Achen (Fz Julich): currently interested to join
JSC «Afrikantov OKBM»: currently interested to join

## Slide 7: Current Status
IRSN prepared a ‚scaling study‘ which
  Considers plant studies provided by IRSN, PSI and IBRAE about the steam and H2 loads to certain PWR designs
  Transposing the information to a generic 1000 MWth plant containment size, which is also determined
  Conducted study to determine H2 distribution for a several conditions for the ‚reference size‘
IRSN is in the process of determination of the ranges of initial and boundary conditions of the tests to be conducted in TOSQAN, MISTRA, PANDA and KMS like facility

## Slide 8: Current Status
QA document is issued
Web site is operational
Facility Description Documents issued
One paper will be published in NURETH 2011